Relationships among Weather, Glacial Ablation, and Fluvial Processes, Svalbard, Norway

A thesis submitted in partial fulfillment of the requirements for the degree of

Bachelor of Science in Geology

from the College of William and Mary in Virginia,

by

EMILY SLYE GERCKE

Williamsburg, Virginia

May 2006

Table of Contents

List of Figures……………………………………………………………………………..3

List of Tables……………………………………………………………………………...4

Abstract……………………………………………………………………………………5

Introduction………………………………………………………………………………..6

Geographic and Geologic Setting…………………………………………………8

Climatic Setting…………………………………………………………………...8

Previous Studies………………………………………………………………….10

Methods…………………………………………………………………………..………13

Weather…………………………………………………………………..………13

Ablation……………………………………………….……………………….…14
	Stream Parameters……………………………………………………….………14

Results……………………………………………………………………………………16

Ablation………………………………………………………..…………………16

Weather and Stream Dynamics…………………………………………..………19

Discussion…………………………………………………………………..……………25

Acknowledgements………………………………………………………………………29

References………………………………………………………………………………..30

List of Figures

Figure 1: Location map of Svalbard and the Linné valley……………………………...…7

Figure 2: 2005 sattelite photo of the Linné valley……………………………………...…7

Figure 3: The geology of the Linné valley ……………………………………………..…9

Figure 4: Photos of data collection techniques used……………………………………..15

Figure 5: Site map of ablation stakes and glacier temperature loggers…………….……15

Figure 6: Bar graph comparing 2004 and 2005 ablation seasons……………………......17

Figure 7: High-resolution ablation data from level loggers…………………………...…18

Figure 8: Average temperature vs. ablation per day……………………………….…….20

Figure 9: 1995 aerial photograph of the Linné glacier with historical terminus 	positions…………………………………………………………………..……...21

Figure 10: Time series plots of stream parameters and weather data………………..…..22

List of Tables

Table 1: Total ablation between measurements……………………………………….…17

Table 2: Historical retreat rates for the Linné glacier……………………………………20

Table 3: Results of stream and weather autoregressions……………………………...…24

Abstract

The influence of weather factors on glacier ablation is a topic of much debate in arctic scientific literature.  Corresponding studies of glacier meltwater and stream suspended sediment characteristics are also common, but results vary with study location.  This study aims to characterize the Linné valley in terms of seasonal glacial and fluvial patterns, and examine the effect of these parameters on sedimentation in Lake Linné.  This study will contribute to the understanding of Linné valley processes and further the ultimate goal of interpreting Holocene climatic changes from lake sediment cores.

During the 2005 field season (July 23rd-August 14th ), weather, stream and glacier ablation data were collected by the Svalbard REU team.  Statistical analyses and physical observations were employed to characterize the relationships between these three physical realms and compare them to expected results as well as previously studied areas.

Throughout the field season, the Linné Glacier melted 0.5 meters on average, causing diurnal fluctuations in stream stage and suspended sediment load.  Relationships between suspended sediment and stream stage are explained by significant autocorrelation results but causal relationships between weather and stream parameters are more complicated due to the effects of lag time.  Efforts to pinpoint direct sources of glacier ablation were less fruitful, partially because of inadequate data collection techniques.  However, analysis of aerial photos documents over 1.3 km of retreat since the end of the Little Ice Age, with a dramatic increase in retreat rate after 1969.  Comparison of physical results to similar studies suggests that the Linné valley conforms to expectations of high arctic cold-based glacier systems.

Introduction

The polar regions of the earth generally experience and exhibit the effects of climate change considerably earlier than mid-latitudes because ice caps and glaciers are susceptible to melting as a result of warmer temperatures.  As climate change awareness increases in the consciousness of the public, continuing emphasis is placed on studies that can provide insight into the causes and effects of a warming climate before they are seen and felt by the majority of the global community.  Because climatic fluctuations in the arctic are magnified, it is important to thoroughly examine physical trends recorded in these areas.

Svalbard, Norway (Figure 1) is a particularly interesting and crucial place to study climate change.  O’Brien et al (1995) have shown that the temperature changes during the interval in the Holocene known as the Little Ice Age were more pronounced in the north Atlantic.  This is because altered atmospheric circulation caused increased flows of cold air from the northeast.  In 1988 Werner confirmed that the Little Ice Age was the largest glacial event of the Holocene for Spitsbergen, the largest island of Svalbard.  Proglacial Lake Linné (Figure 2) provides a sedimentary record stretching to the beginning of the Holocene that could potentially be useful for climatic reconstruction and interpretation of this significant event.

The broad goal of the Svalbard REU program is to accurately interpret sediment cores from Lake Linné.  Sediment layers in the lake are very finely laminated but have not yet been shown to occur as seasonal varves.  In order to correctly explain Lake Linné sediment laminations, we must understand the processes throughout the valley that affect sedimentation in the lake.

Figure 1: Map showing the location of Svalbard and the Linné valley

Figure 2: Satellite photo of the Linné valley.  Lake Linné is in the north central region, the Linné glacier is 8km upstream (south central).

Geographic and Geologic Setting

Svalbard, Norway (78º 12’ N, 15º 40’ E) is an archipelago of glaciated islands midway between the north coast of Norway and the North Pole (Figure 1).  The islands cover 63,000 km2 and are characterized by central ice caps, deep valleys and sharp, steep

mountains.  The western coast is known for its fjords.   Most rocks on the main island Spitsbergen are sedimentary and come from the Tertiary, Carboniferous and Devonian periods.  The basement rock is the Hekla Hoek Formation of the upper Proterozoic.  It was metamorphosed during the Caledonian orogeny and is highly faulted (Christiansen, 2005).  The Linné valley is located on the west-central coast of Spitsbergen and spans the contact between the Proterozic basement rocks to the west and carboniferous strata to the east (Figure 3).  The valley is 15 km long and trends north-south.  The Linné River carries meltwater from the Linné glacier, located at the south end of the valley, to Lake Linné to the north.

Climatic Setting

Svalbard is located at the end of the northernmost branch of the Gulf Stream, which creates a relatively warm climate for its latitude.  The mean annual temperature in

Svalbard is -6ºC, making it ideal for non-temperate glaciers, but the temperature also rises significantly in the summer time.  Thus, a range of glacier types can be observed.  Some glaciers in Svalbard have a combination of temperature regimes that change over time and seasonally (Hagen, et al 1993).  The Linné Glacier is a small cirque glacier that has not been thermally categorized but is assumed to be non-temperate because of its thickness (~43m) and size (1.69 km2) (Hagen et al, 1993).

Figure 3: The geology of the Linné valley.  From Perreault 2006.

Glaciations occurred very early (~650 MY) and very late (2-3 MY) in Svalbard’s geologic history.  The glacial history of the Linné valley was extensively studied by Svendsen and Mangerud in 1992.  During the Younger Dryas (13,000 years BP), the

valley existed as a N-S trending fjord and the valley glacier terminated on the continental shelf of the ocean to the north.  A rapid glacial retreat occurred around 12,500 radiocarbon years BP.  Radiocarbon dates on marine sediments and shells at the bottom of lake cores indicate a marine environment until at least 9,600 years BP (Boyum and Kjensmo, 1980).  Isostatic uplift caused by the retreat of these glaciers isolated the lake at the beginning of the Holocene, at which point lacustrine sediment deposition began.  During the Holocene there were no glaciers in the Linné valley until the Little Ice Age (LIA) that occurred from the 15th-19th centuries.  The Linné Glacier was at its maximum Holocene extent during the Little Ice Age (Mangerud and Svendsen 1990, Werner 1988).  A 40m high moraine remains to document LIA coverage and an oblique aerial photo taken in 1936 shows the glacier at its LIA extent.  Prominent LIA moraines can also be observed on the sides of the valley indicating the presence of cirque glaciers during the LIA and confirming the significance of this cooling event and the accelerated climate warming that has occurred throughout this century (Werner 1993).

Previous Studies

In 1980, Boyum and Kjensmo completed one of the first studies on Lake Linné sediments.  They took a long core of the deep basin and found marine sediments deposited during the Younger Dryas overlain by modern lacustrine sediments.  The authors speculate about potential sediment sources based on down-core compositional changes and loss on ignition techniques.  They conclude that there are several sources of sediment to the lake that should be geochemically distinctive due to the three rock types in the catchment (Boyum and Kjensmo 1980).  Analysis of Lake Linné cores by Werner (1988) demonstrated an inverse relationship between weight percent organic carbon (originating in the central coal/sandstone formation) and carbonate (from the eastern limestones and dolomites) throughout the Holocene.  The variations in carbon content were attributed to changing sediment sources because of glacial retreat.  This conclusion is fragile because carbonate in lake sediments is easily dissolved into the water column and carried out of the lake (Thomas 2005).  Thus down-core carbon analyses may not be useful for reconstructing glacial activity in the valley because the amount of carbonate may be severely underestimated.  Provenance studies completed by Thomas in 2005 and Perreault in 2006 show that certain laminations in the lacustrine sediments can be traced to specific source areas using mineralogical analyses.  Using these methods, Perrault was able to pinpoint specific sediment layers with sources in the carbonate and phyllite units.  However, it is important to note that the Linné River does not have a distinctive mineralogical or geochemical signature (perhaps because it is fed by tributaries that flow over all of the formations) and thus the activity of the glacier cannot be ascertained using this method (Perreault 2006).

The Linné Valley is hydrologically governed by the Linné Glacier, located 8km upstream from the inflow into Lake Linné.  The glacier is relatively small for Svalbard, only 1.69 km2 in area and 0.072 km3 in volume.  No scholarly studies have been carried out on the Linné Glacier, aside from mass balance analyses by the Svalbard REU program in 2004.  Caleb Schiff documented the 2004 mass balance at -1.21 m of water equivalent and observed that the entire glacier was below its equilibrium line altitude.  He estimates the complete melt of the Linné Glacier within 50-60 years (Schiff 2005).

Hodson and Ferguson in 1999 studied suspended sediment transport from glaciers in Svalbard with different thermal regimes.  They believe that it is a mistake to apply generalizations from temperate glacier systems to arctic, cold-based glaciers and set out to discover the fluvial-sedimentological differences between these two types.  They collected similar data to this study (discharge, suspended sediment concentration) and examined seasonal patterns in a warm-based, cold-based and intermediate glacier.  For the cold-based glacier (most comparable to Linné), their study documented significant relationships between discharge and suspended sediment with large diurnal variations.  The relationship between discharge and suspended sediment was not simple (concluded from non-random scatter in bivariate graphs), but Hodson and Ferguson were able to conclude that “suspended sediment entrainment…is strongly responsive to discharge forcing at diurnal time scales” (Hodson and Ferguson 1999).  Suspended sediment entrainment in their cold-based system was largely proglacial due to the absence of a developed inter-glacial drainage system (Hodgkins 1997).  Because the sources of sediment are proglacial rather than subglacial and are not easily exhausted, patterns of increasing sediment availability are noted in suspended sediment data (Hodson and Ferguson 1999).

The specific role of glacier ablation on suspended sediment dynamics has not been studied in this catchment.  In order to interpret sediment laminations, seasonal sediment fluxes from the Linné River need to be better understood.  In addition, meteorological conditions associated with certain sediment characteristics will aid climatic reconstruction.  As part of the Svalbard Research Experience for Undergraduates program, this study aims to 1) quantify and elucidate the relationships among meteorological factors, ablation from the Linné Glacier, and suspended sediment in the Linné River and 2) determine historical ablation rates in order to contextualize the 2004-2005 ablation year and the current climate warming that is occurring.

Methods

Weather

During the 2005 field season, an Onset HOBO® weather station, situated near the south shore of Lake Linné, measured the following meteorological factors: air temperature, relative humidity, barometric pressure, solar radiation, reflected solar radiation, wind speed and direction, precipitation, and soil temperature at 0.5 and 1 m. (Figure 4a).  This station has continuously taken measurements on the half-hour since the

summer of 2003 and is the main source for weather data used here.  Because the weather station is located over 8km away from the Linné Glacier, three other temperature loggers located closer to the glacier were used to supplement weather station data (Figure 5).  The upper and lower glacier temperature loggers failed for part of the field season, but the middle logger located on a remnant nunatak provided the temperature data used in glacier analyses.  In addition, we made daily observations of conditions in the valley and programmed a camera to take a picture of the glacier hourly in order to determine fog conditions.

Ablation

In April 2005 eight ablation stakes made of 6m long galvanized aluminum were installed 250 m apart along the center line of the Linné Glacier (Figure 5).  The stakes are

assumed to be frozen in the ice and the exposed stake height can be measured to determine amount of melt between measurements.  Stake height above snow cover was measured at the time of installation and snow soundings were taken to determine the depth of the snow over the ice surface.  During the 2005 field season, we measured stake height to the nearest half centimeter approximately every 2 days.  Similar data was collected during the 2004 season.

An experimental technique was used to provide a high resolution ablation data set.  At ablation stakes 1, 6 and 8, 3” diameter holes were drilled approximately 1.5 meters into the surface of the glacier (Figure 4c).  Because the glacier melts surficially, the holes are always filled with water, and the water height decreases as the glacier melts.  A level logger that was hung at the bottom of each hole measured the water level every half hour.

Aerial photos taken in 1936, 1961, 1969, 1990 and 1995 were georeferenced to a 2005 satellite photo using GIS software.  Historical terminus positions were traced in order to calculate recession rates.  Glacier area was determined and volume loss was calculated using an equation generalized for Svalbard glaciers (Hagen et al, 1993).

Stream parameters

A stream gauging and suspended sediment sampling station was established just outside the Linné glacier Little Ice Age moraine on the Linné River.  This location is over 1 kilometer from the current terminus of the glacier and it is important to note that it is

Figure 4 (clockwise from left): a. Main weather station in the Linné valley b. The author measuring ablation at stake 8 c. Level logger and bracket for hanging at stake 1 (borehole just visible below tip of logger) d. ISCO® suspended sediment sampling device at LIA moraine gauging station.

Figure 5: Location of ablation stakes and temperature loggers on the glacier.  The main weather station is 8km to the north, near the shore of Lake Linné.

downstream of many recessional moraines and a large mudflat.  Stream discharge was measured manually 8 times using depth probes and flowmeters.   A rating curve was

constructed using stage height measured by an in-stream level logger.  The rating curve regression is poor, so in this study stage height is used as a proxy for stream discharge.  An ISCO® automated sediment sampler collected 200mL water samples from the center of the river every 2 hours for 17 days (Figure 4d).  Samples were filtered through Whatman cellulose papers (0.45 µm), dried and weighed to determine suspended sediment concentration.

Results

Ablation

The 2005 ablation year recorded almost half the amount of ablation measured in 2004 (Figure 6).  On average, the glacier thickness decreased by 0.48 meters, but this varied from 0.38 meters at stake 5 to 0.67 meters at stake 1 (the toe).  Over the observation period, total amount of ablation between measurements varied greatly (Table 1).  However, the amount of ablation at each stake was not proportional to the total ablation (i.e. usually the glacier would melt a lot at one or a few stakes instead of the same or proportionally at all stakes).  Total hand measured ablation over the season was roughly equal to the total level logger measured ablation over the season, verifying the accuracy of both techniques at coarse time scales.

At a 30 minute time scale, glacier level loggers record positive ablation (or accumulation) (Figure 7).  During the field season, we observed no reason to believe that accumulation was actually occurring (there was no frozen precipitation, and temperatures never reached below freezing).  For this reason, level logger ablation data was not used in

Figure 6: Amount of ablation measured by hand during the 2004 and 2005 field seasons.

| Period between observations | Total ablation (m, all stakes) |
| --- | --- |
| 7/24-7/27 | 0.74 |
| 7/27-7/30 | 0.5 |
| 7/30-8/1 | 0.51 |
| 8/1-8/3 | 0.41 |
| 8/3-8/5 | 0.3 |
| 8/5-8/7 | 0.47 |
| 8/7-8/9 | 0.57 |
| 8/9-8/11 | 0.34 |
| 8/11-8/13 | 0.29 |

Table 1: Total amount of ablation (sum of all stakes) for 9 time periods measured.  Note that first two time periods are 3 days long, the rest are two days long.

Figure 7: Level logger ablation curves for stakes 1 and 8, corrected for atmospheric pressure.  Note the increases in ablation ("accumulation").

many analyses.  The series was smoothed in order to remove the accumulation spikes but the time scale became too coarse to use for valuable weather correlations.  In the following discussion, the Linné Glacier is assumed to be the middle factor in translating these weather factors into stream discharge and analyses were carried out accordingly.

In order to examine the direct effects of weather on glacier ablation at larger time scales, we used the hand measured ablation to compare to daily average air temperature and solar radiation value (Figure 8).  None of these regression analyses were significant, in part because of the small number of data points.

Historical retreat rates for the Linné Glacier are illustrated in Table 2 and can be visually observed in Figure 9.  Total retreat after the end of the Little Ice Age in 1936 is 1.3 km, with a dramatic increase in retreat rate after 1969.  During the 2005 ablation season, 1.05% of the Linné Glacier's current volume (758,715 m3 of ice) melted.

Weather and Stream Dynamics

The Linné River transported approximately 54.2 metric tons of suspended sediment to Lake Linné from July 28th to August 11th, 2005.  The data show a strong daily signal in river stage and suspended sediment flux that occurs daily around noon-4pm. (Figure 10a).  A clear response to weather factors is shown in stage and suspended sediment data (Figure 10b, 10c, 10d) but the magnitudes of these changes are independent of one another.  Lag times between weather factors and river characteristics range from zero to six hours.  In order to identify the specific physical parameters that govern suspended sediment supply (via changes in ablation and discharge), statistical techniques were employed.  Simlilar to autocorrelation techniques used in Hodson and

Figure 8: Average temperature between ablation measurements vs. total ablation per day.  Solar radiation graph produces similar regression results.

| Time Period | Amount of retreat (m) | Retreat rate (m/year) |
| --- | --- | --- |
| 1936-1961 | 259 | 10.36 |
| 1961-1969 | 83 | 10.37 |
| 1969-1990 | 395 | 18.81 |
| 1990-1995 | 282 | 56.40 |
| 1995-2005 | 328 | 32.80 |
| 1936-2005 | 1347 | 19.52 |

Table 2: Historical retreat rates for the Linné Glacier.  Note the dramatic increase after 1969.

Figure 9: 1995 aerial photograph of the Linné Glacier with historic terminus positions and 2005 ablation stake locations.

Figure 10 (top to bottom): Time series plots illustrating the relationship between A. river discharge and suspended sediment (note that both high and low discharges can produce the same suspended sediment flux, indicating the independence of magnitude changes) B. air temperature and discharge (note the independence of discharge during a precipitation event- discharge increases even though temperature is falling) C. solar radiation and discharge D.  Solar radiation and suspended sediment flux.

Ferguson 1999, a Prais-Winsten autoregression test was used to determine the relationships between stream parameters and weather.  An autoregression is used to

remove the correlation between subsequent points in a time series dataset.  Stage height was found to be a significant predictor of suspended sediment concentration (β Coefficient: 0.474, Significance: 0.000).  Neither temperature nor solar radiation was shown to significantly predict stage height or suspended sediment concentration (Table 3).  Comparison of the significance values shows that air temperature and solar radiation more accurately predict stage height and not suspended sediment concentration, even though the relationship is statistically non-significant.

To account for magnitude independence yet still analyze for weather and stream interactions, Spearman Rank analyses were performed on stream data that was separated by “discharge day,” the period between the lowest daily stream stage.  Out of 12 days, 11 recorded statistically significant correlations between stage and suspended sediment concentration, mirroring the autoregression results. In general, when the relationship between solar radiation and stage was significant, it followed that solar radiation and suspended sediment concentration were significantly related.  The effect of air temperature on stream parameters was generally not significant.  These analyses were examined for patterns by comparing significance results to average temperature, average solar radiation and amount of precipitation for each discharge day.  Precipitation appears to be a confounding factor for weather and stream correlations but this relationship is not consistent.

|  | Stage Height |  | Suspended Sediment Concentration |  |
| --- | --- | --- | --- | --- |
| Predictor | Regression Coefficient (β) | Significance | Regression Coefficient (β) | Significance |
| Air Temperature | 0.141 | 0.167 | 0.40 | 0.710 |
| Solar Radiation | 0.146 | 0.154 | 0.86 | 0.423 |

Table 3: Results of time-series autoregression tests.  Air temperature and solar radiation are not significant predictors of stream stage height or suspended sediment concentration.

Discussion:

Historical retreat rates calculated for the Linné Glacier are consistent with the retreat rates calculated by Schiff in 2005.  If ablation rates exceed or maintain 2005 rates,

the Linné Glacier will completely disappear in less than 95 years.  Because the glacier melted almost twice as much in 2004, estimates of complete melt are at least twice as long as reported by Schiff.  Although high-resolution ablation data were not collected in 2004 and meteorological factors were not compared to stream data, many researchers in this area (Schiff 2005, Thomas 2005, the author) speculate about the most important factor in glacier ablation.  The main difference between the two field seasons was the significant difference in amount of precipitation.  In 2004, 84.4 mm of rain fell between July 23rd and August 9th , while in 2005, the Linné valley received only 19.2 mm of precipitation (July 23rd – August 14th).  The fact the glacier melted almost twice as much during the 2004 field season may be purely coincidental with the increased amount of precipitation.  However, physical observations of the glacier by Thomas and Schiff during 2004 and the author in 2005 point to increased ablation on rainy days.  Because the temperature of rain is generally warmer than glacier ice, surficial melting occurred quickly and expansively, making the entire surface of the glacier very slick (crampons were necessary for travel).  On warm days, the surface of the glacier was a crunchy, popcorn-like consistency that could be walked upon without crampons, indicating that surficial melting wasn’t as extensive.  However, without proper data (high resolution ablation, precipitation directly on glacier) from both seasons, we cannot conclusively determine a causal relationship.

We were not able to directly compare fine-resolution ablation data to weather parameters.  Because level logger data recorded accumulation and did not appear to respond to weather factors when graphed, we assumed that either glacier ablation proceeds with little response to weather conditions and has minimal direct effect on river discharge, or more likely, the technique we used does not accurately record glacial conditions at small time scales.  Because the Linné River stage has a visible relationship to weather factors such as temperature and solar radiation (Figure 10b, 10c), and there is no other physical means of translating weather parameters into stream discharge, we presumed the latter.  In the field, we observed various possible mechanisms for this instrumental error.

Magnitude independence in weather and stream data could stem from many factors.  Others (Hodson, et al 1998) have suggested that sediment source can change significantly over the course of a season and the possibility exists for this to occur on daily timescales in a complicated system.  Because a high suspended sediment concentration can be achieved by high stage on one day and low stage on another, the exhaustion and replenishment of sediment sources may be a feasible explanation.  However, there is no consistent pattern of low stage, high sediment concentration followed by high stage, high sediment concentration.  When suspended sediment data were separated according to position on the hydrograph (rising/falling limb), linear regression did not document a significant relationship to stage.

In general, suspended sediment characteristics in the Linné system conform to the observations made by Hodson and Ferguson (1999) in their study of another Svalbard cold-based glacier system.  In such systems, the presence of cold layers of ice at the base of the glacier reduces the amount of meltwater that can reach the base of the glacier and restricts the development of englacial or subglacial drainage structures.  Sediment sources then, are proglacial and sediment supply is not exhausted throughout the season.  In the Linné valley, a diurnal signal in river parameters was always present but highly variable throughout the season, just as Hodson and Ferguson observed in their cold-based system.  There is no evidence for seasonal exhaustion of sediment supply although the possibility exists that our observation period was not long enough to observe this.  However, other physical evidence (clear meltwater proximal to the glacier, proglacial mudflats) also suggests that sediment entrainment in meltwater is proglacial.

There seem to be no discernable patterns to the statistically significant relationships between weather and stream data.  One would expect relationships between stage/suspended sediment and temperature/solar radiation to be significant during days with high ablation and no precipitation (which would dilute the effect of glacial meltwater in the stream).  However, on the day with the most precipitation (3.2 mm on August 3rd), solar radiation had a statistically significant relationship with both stage and suspended sediment concentration.  It is important to remember that the use of stage instead of discharge in these analyses may account for some error; the poor quality of the rating curve in this area disabled the production of accurate discharge data.

The lack of statistically significant relationships between temperature and stream parameters may also indicate that in this case glacier ablation is not positively related to air temperature.  This is contrary to previous studies that suggest that temperature is the most important factor in glacier ablation (Szafraniec 2002), however most studies directly measure ablation; here we are forced to infer melting based on stream responses.  On the Linné Glacier, the effect of temperature on ablation may be overshadowed by the influence of cloud cover or regional shading by surrounding mountain peaks.  Warm days with lots of cloud cover might result in reduced ablation.  Solar radiation corresponds to stream parameters because it is a better indication of sunny days.  The fact that ablation rates at each stake were not proportional to each other also speaks to the important role of micro-scale features like topography, dark colored debris on the surface of the ice, or other factors. The main role of weather in this system is generalized direct melting of glacier ice to supply discharge for proglacial entrainment of sediment.

Suspended sediment relationships to weather factors were insignificant most likely because there is a long lag time associated with the transition from high temperatures to glacier ablation to stream discharge to sediment entrainment.  Because stream discharge comes into play earlier in the equation, the time lag is short enough for the autoregression to document significant results.  Because the time lag between peak temperature/solar radiation and suspended sediment concentration is not consistent, we were not able to correct for this.

Acknowledgements:

Many thanks to my advisor Greg Hancock, along with Rowan Lockwood and Timothy Russell at William and Mary for their continuous support and patient help with bumps in the road.  Thanks also to the Svalbard REU leaders Steve Roof, Mike Retelle and Al Werner, and my fellow REU team Nora Matell, Fran Moore, Brooks Motley, Lauren Perrault, Carlos Szembeck, and Brian Yellen for fantastic company for five weeks in the high arctic.  Thanks to the NSF (Arctic Natural Sciences and Paleoclimate Programs) for funding this research.

References:

Boyum, A. and Kjensmo. 1980, Post-glacial sediments in Lake Linnevatn, Spitsbergen: Arch Hydrobiol, v. 88, p. 232-249.

Christiansen, Hanne H. 2005, Brief Outline of the Geological History of Svalbard.  Lecture given 7/15/05.

Hagen, J., Liestol, O., Roland, E., and Jorgensen, T. 1993, Glacier Atlas of Svalbard and Jan Mayen. Oslo, Norway: Norsk Polarinstitutt.

Hodgkins, Richard. Glacier Hydrology in Svalbard, Norwegian High Arctic: Quaternary Science Reviews, v. 16, 1997.

Hodson, Andrew J. and Ferguson, Robert I. 1999, Fluvial Suspended Sediment Transport From Cold and Warm-Based Glaciers in Svalbard: Earth Surface Processes and Landforms, v. 24, p. 957-974.

Hodson, Andrew, et al. 1998, Suspended sediment yield and transfer processes in a small High-Arctic glacier basin, Svalbard: Hydrological processes, v. 12, p. 73-86.

Mangerud, J. and Svendsen, J.I. 1990, Deglaciation chronology inferred from marine sediments in a proglacial lake basin, western Spitsbergen, Svalbard.  Boreas 19, 249-272.

O’Brien, S., Mayewski, P.A., Meeker, L.D., Meese, D.A., Twickler, M.S., and Whitlow, S.I. 1995, Complexity of Holocene climate as reconstructed from a Greenland ice core: Science, v. 270, p. 1962-1964.

Perreault, Lauren. 2006, Mineralogical analyses of sediment source changes to Linnévatnet, Svalbard.  36th International Arctic Workshop, Program and Abstracts.  Additional personal contact.

# Schiff, Caleb, 2005, Unsustainable glacier ablation at 78( N latitude, Linnébreen, Svalbard.  Geological Society of America Abstracts and Programs.  Additional personal contact.

Svendson, J.I and Mangerud, J. 1992, Paleoclimatic inferences from glacial fluctuations on Svalbard during the last 20,000 years: Climate Dynamics. v. 6, p. 213-220.

Szafraniec, Joanna. 2002, Influence of Positive Degree-days and Sunshine Duration on the Surface Ablation of Hansbreen, Spitsbergen Glacier: Polish Polar Research, vol. 23.

Thomas, E.K. 2005, Using geochemical evidence to determine provenance in a high-Arctic glacier-fed lake, Linné valley, Svalbard Norway [Undergraduate Honors Thesis]: Smith College.

Werner, A. 1988, Holocene glaciation and climate change, Spitsbergen, Svalbard [Ph.D. Dissertation]: University of Colorado at Boulder.

Werner, A. 1993, Holocene moraine chronology, Spitsbergen, Svalbard: lichenometric evidence for multiple Neoglacial advances in the Arctic: The Holocene, v. 3, p. 128-137.